## Slide 1: Network-software interfaces
Boris Pismenny, Haggai Eran, Aviad Yehezkel, Liran Liss, Adam Morrison, and Dan Tsafrir
Boris Pismenny | Adam Morrison | Dan Tsafrir
 | Tel-Aviv University | Technion
Notes: tutorial on how NICs and accelerators being integrated into the OS and software.

## Slide 2: Overview
Technology trends
Existing approaches
  Software interfaces
  Hardware interfaces
Future

## Slide 3: Trend: NICs are cheaper than CPUs
Paravirtual remote I/O by Kuperman et al., ASPLOS’16
2x CPU cores—4x price
4x NIC speed—only 2x price
Notes: I’d like to start from talking about NIC and CPU prices and I’m going to show that NIC upgrades are cheaper than CPU upgrades.
The following figure shows this trend by comparing the ratio of added hardware to the added cost. Every point represents a pair of CPUs in blue or a pair of NICs in red that differ only in one parameter other than price. For CPUs, the pair differs in the number of cores and the price, and for NICs, the pair differs in the network speed and the price. For example, (click) the blue point at (4,2) represents a pair of CPUs such that it is possible to double the number of cores by quadrupling the price. On the other hand, (click) the red point in (2,4) shows that it is possible to quadruple NIC speed by only doubling the cost. Since all the points above the break-even line are NICs and all the points below it are CPUs, we conclude that it is more profitable to invest in improving NIC speeds than in improving the number of CPU cores. Moreover, CPUs are the most expensive component in servers. So, we would like to find ways to help CPUs manage with the growing speed of NICs.
90s

## Slide 4: Trend: NIC offloads are free
Gen. | Year | Added offloads
3 | 2011 | First Ethernet driver Segmentation Checksum
4 | 2014 | I/O page faults (ASPLOS’17)
5 | 2016 | Multipacket descriptors (OSDI’23) NVMe emulation UDP segmentation offload
6 | 2019 | AES-XTS encryption offload
Same price different offloads
Autonomous NIC offloads by Pismenny et al. , ASPLOS’21 best paper
Notes: Not only is it more cost effective to upgrades NICs instead of servers, but NIC offloads are often practically free, and this is what we show next.
The following table presents 4 generations of Mellanox ConnectX NICs between 2011 and 2019 (CX3 to CX6), each generation adds new offloads that improve performance (ODP, Enso, XTS). <Click> Now if we look at the prices of these NICs, then we can observe an interesting phenomena where in many cases what determines the price is not the NIC’s generation and its offloads but rather the number of NIC ports and their speed. So we conclude that offloads are often added for free.

## Slide 5: Trend: per-core bandwidth to saturate I/O
Notes: Mention: TCP baremetal is 25Gbps, and VM is 10Gbps, DPDK is higher.
Message: offload when we can and otherwise make CPUs more efficient
So, what’s the takeaway from this analysis?
1) Don’t go through memory, even zero-copy isn’t good enough since the I/O device reads/writes to memory. DCA is a possible solution.
2) CPUs struggle to saturate line-rate and I/O offloads are necessary.
TODO: do side-by-side slides and write the takeaways

## Slide 6: Existing software interface optimizations
Batching
Zerocopy
Memory BW bottlenecks
Living alongside memory BW bottlenecks
Solving memory BW bottlenecks
Unmodified socket application Only kernel/hypervisor changes
App rewrite

## Slide 7: Batching
User/Kernel and VM/hypervisor
  TCP CORK and Nagle’s algorithm
Jumbo frames (1.5KB  9KB)
Segmentation and aggregation offloads (64KB  185KB)
Doorbell, desciptor, completion batching
Interrupt batching
  Adaptive NIC Interrupt coalescing
  Optimizing Storage Performance with Calibrated Interrupts (OSDI’21)
Notes: Batching is a very basic and straightforward technique to improve throughput at the cost of latency. I think that Nagle’s algorithm demonstrates this really well… Jambo packets can be used in closed networks to send more data using each packets. Segmentation and aggregation offloads provide similar benefits to Jumbo even when the MTU is smaller. They do this by sending
Cork is when a packet is being sent by the NIC to the network, so TCP can aggregate more data of the same flow being sent by the app.
Segmentation up to 64KB (max ipv4 datagram), today segmentation up to 256KB (BIG_TCP)
Segmentation and aggregation need checksum offload
Driver software and hardware use batching too: for doorbell, descriptor and completion batching.
Interrupts: send them when needed based on application-layer information
Still evolving: latency/throughput tension creates a tra

## Slide 8: Zerocopy (TCP)
recvmsg (page remapping)
sendmsg (MSG_ZEROCOPY)
io_uring

## Slide 9: Kernel TLS
App
TCP/IP
NIC
TLS
TLS message header/trailer
TCP header
Baseline
data
encrypt
user
kernel
copy
H | H | enc(data) | T
H | H | enc(data) | T
H | enc(data) | T

## Slide 10: Kernel TLS
App
TCP/IP
NIC
TLS
TLS message header/trailer
TCP header
Baseline
data
encrypt
user
kernel
copy
Kernel TLS
user
kernel
encrypt+copy
data
H | H | enc(data) | T
H | H | enc(data) | T
H | H | enc(data) | T
H | H | enc(data) | T
H | enc(data) | T
H | enc(data) | T

## Slide 11: Zerocopy (TCP)
Recvmsg (page remapping)
Sendmsg (MSG_ZEROCOPY)
Io_uring
Kernel TLS
In-app copies
  zIO: Accelerating IO-Intensive Applications with Transparent Zero-Copy IO (OSDI’22)
Serialization using scatter-gather
  Cornflakes: Zero-Copy Serialization for Microsecond-Scale Networking (SOSP’23)
Accelerator device memory
  GPUnet (OSDI’14)
  High-throughput and Flexible Host Networking for Accelerated Computing (OSDI’24)

## Slide 12: Zerocopy receive is sub-optimal
Zerocopy receive struggles to fill contiguous application buffers
1MiB image
Chart: 
| 1st Qtr | 2nd Qtr | 3rd Qtr | 4th Qtr
Sales | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
Rx
4KiB chunk 1
4KiB chunk 1
4KiB chunk 1
4KiB chunk 1
4KiB chunk N
4KiB chunk 2
4KiB chunk 1
Notes: Suppose we want to fill a 1MiB buffer with some input, say an image. We use zerocopy, and for example with io_uring, (click) we point Rx ring descriptors to buffers the together compose the 1MiB. Ideally, data arrives in-order and fills the 1MiB image as expected (click). But, if data arrives out-of-order or retransmissions happen (click), then we need to fallback to copying or to use an accessor function that can find the location of each byte of our image.

## Slide 13: Possible solution: direct data placement (DDP)
Write arbitrary long data only in its correct destination
  RDMA
  TCP?
Yes, using Autonomous NIC offloads

## Slide 14: Trend: I/O > memory BW
Notes: But zero-copy is kind of a dead-end, because as the following figure shows, if we want to fully saturate server I/O then we can’t even DMA data to memory, and this also further motivates the need for clever I/O acceleration.

## Slide 15: Living alongside memory BW bottlenecks
Caladan: Mitigating Interference at Microsecond Timescales (OSDI’20)
  Identify high memory bandwidth
  Backpressure compute: reallocate cores
Host Congestion Control (SIGCOMM’23)
  Identify high memory bandwidth
  Backpressure network: TCP explicit congestion notifications
  Backpressure compute: reduce core memory bandwidth using Intel MBA

## Slide 16: Solving memory BW bottlenecks using DCA
Direct Cache Access for High Bandwidth Network I/O (ISCA’05)
  DMA to/from CPU LLC (Intel DDIO)
Disk|Crypt|Net: rethinking the stack for high-performance video streaming (SIGCOMM’17)
  Sendfile over TLS; keep working-set in LLC

## Slide 17: Existing hardware interface optimizations
Multicore
Virtualization
Packet layer
Transport layer
Application layer
Notes: 15m

## Slide 18: Multicore and multiqueue transmit
Goal: schedule packet transmission from multiple cores fairly and efficiently
Single centralized queue – bottleneck
Hash based queue selection – imbalance
Large batches of packets – imbalance
Chart: 
| 1st Qtr | 2nd Qtr | 3rd Qtr | 4th Qtr
Sales | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
centralized scheduler
Chart: 
| 1st Qtr | 2nd Qtr | 3rd Qtr | 4th Qtr
Sales | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
Chart: 
| 1st Qtr | 2nd Qtr | 3rd Qtr | 4th Qtr
Sales | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
hash function
Chart: 
| 1st Qtr | 2nd Qtr | 3rd Qtr | 4th Qtr
Sales | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
Chart: 
| 1st Qtr | 2nd Qtr | 3rd Qtr | 4th Qtr
Sales | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
load-aware hash function
64B pkt
1.5KB pkt

## Slide 19: Multicore and multiqueue transmit
Goal: schedule packet transmission from multiple cores fairly and efficiently
Single centralized queue – bottleneck
Hash based queue selection – imbalance
Large batches of packets – imbalance
Titan: Fair Packet Scheduling for Commodity Multiqueue NICs (ATC’17)
  Dynamic batching and select queue based on load
Loom: Flexible and Efficient NIC Packet Scheduling (NSDI’19)
  Offload hierarchical packet scheduler to NIC

## Slide 20: Multicore and multiqueue receive
Goal: spread incoming packets evenly to cores
Dispatcher core – bottleneck
  Shenango: Achieving High CPU Efficiency for Latency-sensitive Datacenter Workloads (NSDI’19)
RSS hash or steer to a specific core – imbalance
Chart: 
| 1st Qtr | 2nd Qtr | 3rd Qtr | 4th Qtr
Sales | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
centralized dispatcher
Chart: 
| 1st Qtr | 2nd Qtr | 3rd Qtr | 4th Qtr
Sales | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
Chart: 
| 1st Qtr | 2nd Qtr | 3rd Qtr | 4th Qtr
Sales | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
hash function

## Slide 21: Multicore and multiqueue receive
Goal: spread incoming packets evenly to cores
Dispatcher core – bottleneck
  Shenango: Achieving High CPU Efficiency for Latency-sensitive Datacenter Workloads (NSDI’19)
RSS hash or steer to a specific core – imbalance
Hardware load-balancing based on load – mandates transport offload
  RPCValet: NI-Driven, Tail-Aware Balancing of us-Scale RPCs (ASPLOS’19)
  The NeBuLa RPC-Optimized Architecture (ISCA’20)
  RingLeader: Efficiently Offloading Intra-Server Orchestration to NICs (NSDI’23)

## Slide 22: Multicore Rx memory consumption problem
Queue
  Per-core
  Per-VM
  Per-app
  Per-priority
Queue depth
  Increases with speed

## Slide 23: Trend: LLC size
23
Chart: 
| 2007 | 2014 | 2020
LLC | 12288 | 38400 | 78848
Size (MB)
LLC

## Slide 24: Trend: NIC Rx size > LLC size
Chart: 
Ring per core | 3072 | 23040 | 344064
LLC | 12288 | 38400 | 78848
4x
per-core ring
LLC
Size (MB)

## Slide 25: Trend: NIC Rx size > LLC size
Chart: 
All rings | 49152 | 1179648 | 6291456
Ring per core | 3072 | 23040 | 344064
LLC | 12288 | 38400 | 78848
Size (MB)
78x
max rings
per-core ring
LLC

## Slide 26: Multicore Rx memory consumption solutions
ShRing: Networking with Shared Receive Rings (OSDI’23)
  Share an Rx ring between independent cores with synchronization on buffer reposting

## Slide 27: ShRing: Networking with Shared Receive Rings (OSDI’23)
core 1
.
.
.
core N
Chart: 
| 1st Qtr | 2nd Qtr | 3rd Qtr | 4th Qtr
Sales | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
memory
NIC
.
.
.
shared receive ring
completion ring 1
Chart: 
| 1st Qtr | 2nd Qtr | 3rd Qtr | 4th Qtr
Sales | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
Chart: 
| 1st Qtr | 2nd Qtr | 3rd Qtr | 4th Qtr
Sales | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
D
Chart: 
| 1st Qtr | 2nd Qtr | 3rd Qtr | 4th Qtr
Sales | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
completion ring N
.
.
.
Chart: 
Packet
Chart: 
| 1st Qtr | 2nd Qtr | 3rd Qtr | 4th Qtr
Sales | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
Chart: 
| 1st Qtr | 2nd Qtr | 3rd Qtr | 4th Qtr
Sales | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
D
D
Packet
Packet
D
D
D

## Slide 28: Multicore Rx memory consumption solutions
ShRing: Networking with Shared Receive Rings (OSDI’23)
  Share an Rx ring between independent cores with synchronization on buffer reposting
Disentangling the Dual Role of NIC Receive Rings (under submission)
  New Rx ring design obviates the need for synchronization
Making Kernel Bypass Practical for the Cloud with Junction (NSDI’24)
  Share an Rx ring between cores using a coordinator core to repost buffers
Intel ENQCMD
  Software writes descriptors and hardware handles conflicts

## Slide 29: Virtualization
Paravirtualization  SRIOV
Inerposition problem
Pinned VM memory
Live migration
VM 1
VM N
Hypervisor
virtio
virtio
inter-VM switch
NIC driver
NAT
firwall
encryption
VXLAN
conntrack
metering
Phyiscal NIC
VM 1
VM N
Hypervisor
VF driver
VF driver
NIC driver
Physical NIC
inter-VM switch
NAT
firwall
encryption
VXLAN
conntrack
metering
 inter-VM switch offload
 Page Fault Support for Network Controllers (ASPLOS’17)
 SRIOV live migration

## Slide 30: Network functions (NFs)
Inter-VM switch offload + hairpin = NF offload
  Eliminates all host overheads: CPU, memory, and PCIe
  Struggles to scale with flows
  Limited programmability
DPDK
  Memory bandwidth bottleneck
The Benefits of General-Purpose On-NIC Memory (ASPLOS’22)
  Store packet payload in ASIC NIC memory to save PCIe and host memory traffic

## Slide 31: The benefits of General Purpose on-NIC memory (ASPLOS’22)
Leave data on NIC memory (nicmem)
Copy only metadata
… data
…
PCIe
CPU
NIC
srcIP=172.16.1.100 dstIP= 172.16.2.1
srcMAC
dstMAC
newSrcMAC newDstMAC
Notes: Our main idea is to eliminate the cost of moving data by leaving it on-NIC memory. Meanwhile, we pass only message metadata to the host for processing. By doing this, we avoid the costs associated we data movers.

## Slide 32: Network functions (NFs)
Inter-VM switch offload + hairpin = NF offload
  Eliminates all host overheads: CPU, memory, and PCIe
  Struggles to scale with flows
  Limited programmability
DPDK
  Memory bandwidth bottleneck
The Benefits of General-Purpose On-NIC Memory (ASPLOS’22)
  Store packet payload in ASIC NIC memory to reduce PCIe and host memory traffic
Enso: A Streaming Interface for NIC-Application Communication (OSDI’23 best paper)
  Streaming Rx descriptor and batched notifications to reduce PCIe traffic

## Slide 33: Enso: A Streaming Interface for NIC-Application Communication (OSDI’23 best paper)
Streaming Rx descriptor
Batched notifications
Map Tx and Rx to same memory to avoid copying
RX
PKT 1
PKT 2
PKT 3
PKT 4
CPU
NIC
RX/TX

## Slide 34: Transport offloads
Dependent NIC offloads (TCP offload engines)
  TCP offload is a dumb idea whose time has come (HotOS’03)
  Complex, evolving, security sensitive, niche

## Slide 35: Transport offloads
Dependent NIC offloads (TCP offload engines)
AccelTCP: Accelerating Network Applications with Stateful TCP Offloading (NSDI’20)
  Goal: offload only connection setup/teardown and splicing
  End result: full TOE
NIC
TCP
splice()
connection 1
connection 2

## Slide 36: Transport offloads
Dependent NIC offloads (TCP offload engines)
AccelTCP: Accelerating Network Applications with Stateful TCP Offloading (NSDI’20)
  Goal: offload only connection setup/teardown and splicing
  End result: full TOE
Why do we want TOEs?
  Accelerate application computation

## Slide 37: Transport offloads
Dependent NIC offloads (TCP offload engines)
AccelTCP: Accelerating Network Applications with Stateful TCP Offloading (NSDI’20)
  Goal: offload only connection setup/teardown and splicing
  End result: full TOE
Why do we want TOEs?
  Accelerate application computation
Can we accelerate app computation without offloading TCP?
  Yes! Autonomous NIC offloads (ASPLOS’21 best paper)

## Slide 38: Autonomous NIC offload: TLS
App
TCP/IP
NIC
TLS
TLS message header/trailer
TCP header
Autonomous TLS offload
H | data | 0
data
H | H | data | 0
H | H | enc(data) | T
copy
user
kernel
Kernel TLS
user
kernel
encrypt+copy
data
H | H | enc(data) | T
H | H | enc(data) | T
H | enc(data) | T
encrypt

## Slide 39: When computation is autonomously offloadable?
Autonomous TLS offload
H | data | 0
data
H | H | data | 0
H | H | enc(data) | T
copy
user
kernel
encrypt
App
TCP/IP
NIC
TLS
Can be computed incrementally
Byte-granular input
Size preserving output
Many computations fit this requirement
  encryption
  decryption
  digest
  direct data placement
  pattern matching
  deserialization

## Slide 40: When L5P is autonomously offloadable?
Autonomous TLS offload
H | data | 0
data
H | H | data | 0
H | H | enc(data) | T
copy
user
kernel
encrypt
App
TCP/IP
NIC
TLS
The protocol message header must contain:
  Message length field
  Plaintext magic pattern (version/opcode)
Many protocols fit this requirement
  http/2
  memcached
  iscsi
  smb
  thrift
  grpc
  nbd

## Slide 41: Conclusion
Technology trends create an opportunity to rethink host networking
CPUs are slow and expensive whereas NICs are fast and cheap
Memory is a key bottleneck for both CPUs and NICs
Use NICs to offload when possible and otherwise make CPUs more efficient
Notes:   We saw several technology trends that I believe are going to remain true for the next few years. These trends present an opportunity to rethink various aspects of the network stack, and we saw several examples of works that do that and the tradeoffs involved. We also discussed some emerging technologies and use-cases that present new opportunities. Two key trends are: (1) CPUs are expensive and slow whereas NIC speeds outpace CPU network processing speeds and their relative price is cheaper; and (2) memory is a key bottleneck for CPU and I/O. Based on these trends, I think that we should offload when we can, and otherwise make CPUs more efficient. My work follows this approach.